brake pads replacement rear F Type R 2016 How To

Ok I got the Porterfield R4S rear pads changed today. My car has 3400 miles. I didnt like the amount of dust from the OEM.

AP1750 FRONT 380MM
AP1753 REAR 376MM

Directions:

1/ Put the car in brake maintenance mode. Ignition on, push the hand brake button down and hold for 2 secs, press accelerator to the floor and hold 2 secs turn ignition off/on and release accelerator and hand brake button. Dash should now read Brake Maintenance Mode. This retracts the EPS motors to allow you to push the piston back in. No tools needed.
2/ Remove wheel, clean wheel and caliper. 
3/ Tie the caliper with wire to the upper suspension arm see pic.
4/ Undo 2X 15mm bolts and swing the caliper out, protect with a rag.
5/ Now push the piston back in with the old pads in place. It moves fairly easy. 
6/ Remove the outside pad first with a flat head screw driver.
7/ Remove the inside pad and with a small flat head screw driver pry off the wear sensor from the bottom edge (passenger side only USA). Clean caliper,
8/ Compare your new pads with the old ones to make sure they are an exact match.
9/grease the back of the new pads with anti squeal grease only on the contact points.
10/ Replace the outside pad first. They push in easy or use pliers to compress the little spring clip on the pad.
11/ Install the inside pad. Put a bit of wood between the pads to hold in place makes it easier to compress that spring clip and push into place.
12/ Put caliper on disc, replace both 15mm bolts torque to 115Nm/85ft lbs
13/ Attach the wear sensor wire, it just pushed on the piston side pad.
14/ Take the car out of brake maintenance mode. Ignition on, pull the hand brake button up and hold for 2 secs, press accelerator to the floor and hold 2 secs turn ignition off/on and release accelerator and hand brake button. Dash should now clear Brake Maintenance Mode.

Done 40min a side. First will take the longest, so start on the drivers side i.e side with no sensor. Much easier that the fronts that I also did a write up for.

Attached Thumbnails

Brake pads replacement front F Type R HOW TO

Ok I got the Porterfield R4S front pads changed today. My car has 3400 miles. I didnt like the amount of dust from the OEM.

AP1750 FRONT 380MM
AP1753 REAR 376MM

So here how I did it.

1/ Remove wheel, clean wheel and caliper. Turn sheering wheel to expose the caliper for easy access.
2/ Tie the caliper with wire to the upper A suspension arm.
3/ Undo 15 bolts and swing the caliper out, protect with a rag.
4/ I did not remove the springs on the caliper bracket no need and I'm told they are a PITA to put back
5/ Now push the pistons back in with the old pads in place. They move fairly easy. Standard compress tool no use with these calipers.
6/ Remove the outside pad first with a flat head screw driver.
7/ Remove the inside pad and with a small flat head screw driver pry off the wear sensor from the bottom edge (drivers side only USA). Clean caliper, grease the back of the new pads with anti squeal grease. Note the OEM ones are really greased up!! and there was chunks of grease and brake pad dust yucky mess!!
8/ Compare your new pads with the old ones to make sure they are an exact match 
9/ Replace the piston side pad first. Reconnect the sensor it just pushes in. Use a flat head screw driver to compress the spring (top & bottom) see photo first gap on the left below where I have the red wire tired.
10/ Install outside pad use flat head screw driver again to compress the spring and a couple of flat bits of wood between to hold the pads in place and push the pad clips into the holes.
11/ Put caliper on disc, replace both 15mm bolts torque to 115Nm/85ft lbs

Done 40min a side first will take the longest so start on the near side. i.e side with no sensor.

Attached Thumbnails