Actually they’re broken inside, grab the electrical connector for the high beams after you remove the radiator cover, if they flop around they’re broken inside, if they’re firm and don’t move they’re ok then you can go have them reprogrammed or check the height sensors on the suspension, making sure it didn’t come unhooked.

If yours are flopping they may be totally broken top and bottom, the screw trick will still work, but you use a much longer screw to basically pin the inside to the back and hold it steady. Or you can pull the light, put it in the oven at 250 F. for 10 minutes, this softens all the urethane so you can easily pull it apart and TRY to repair it. I’ve used structural epoxy on other assemblies like X type and XJ's it works great. But for some reason I haven’t gotten good results on the S type.

For those of you with broken headlights, here’s a fast and good fix that works. If your headlights are broken and pointing down. Take 2 screws and install through the clear lens behind the rubber cover. Drill a Hole first so the plastic does not crack. See picture, the idea is to pin the assembly back to take the place of the pin that broke inside. A screw about 1" long works best if only the top post is broke, if totally broken top and bottom as the unit’s I fixed in the pictures, you’ll need longer screws, about an 1 1/2". Some have a chrome piece you screw into till it touches, these had a white plastic piece with a recessed hole that the screw went into and held.