JAGUAR XK – TECHNICAL DATA

XK Coupe 	XKR Coupe 	XK Convertible 	XKR Convertible	XKR Coupe

5.0L V8 NA	5.0L V8 SC	5.0L V8 NA	5.0L V8 SC	with Speed Pack						5.0L V8 SC

ENGINE & TRANSMISSION

Engine Capacity (litres) 	5.0 	5.0 	5.0 	5.0	5.0

Engine Capacity (cc) 	5000 	5000 	5000	5000	5000

Cylinders 	8 	8	8	8	8

Valves per Cylinder 	4 	4 	4 	4	4

Compression Ratio	11:5:1 	9:5:1	11:5:1	9:5:1	9:5:1

Bore Stroke/mm 	92.5/93.0 	92.5/93.0	92.5/93.0	92.5/93.0	92.5/93.0

Bore Stroke/inch 	3.64/3.66 	3.64/3.66	3.64/3.66	3.64/3.66	3.64/3.66

Transmission Final Drive Ratio 	3:31:1 	3:31:1	3.31:1 	3.31:1	3.31:1

Transmission 	6-speed automatic 	6-speed automatic 	6-speed automatic 	6-speed automatic	6-speed automatic

1st 	4.17 : 1 	4.17 : 1 	4.17 : 1 	4.17 : 1	4.17 : 1

2nd 	2.30 : 1 	2.30 : 1	2.30 : 1	2.30 : 1	2.30 : 1

3rd 	1.52 : 1 	1.52 : 1	1.52 : 1 	1.52 : 1	1.52 : 1

4th 	1.14 : 1	1.14 : 1 	1.14 : 1 	1.14 : 1	1.14 : 1

5th 	0.87 : 1 	0.87 : 1  	0.87 : 1  	0.87 : 1	0.87 : 1

6th 	0.69 : 1 	0.69 : 1	0.69 : 1 	0.69 : 1	0.69 : 1

Rev 	3.40 : 1 	3.40 : 1 	3.40 : 1 	3.40 : 1	3.40 : 1

PERFORMANCE

Fastest 0-60 mph (seconds) (Estimate) 	5.2 	4.6 	5.3 	4.6	4.6

Fastest 0-100 kph (seconds) (Estimate) 	5.5 	4.8 	5.6 	4.8	4.8

Fastest 50-70 mph (seconds) (Estimate) 	2.5 	1.9 	2.5 	1.9	1.9

Fastest 1/4 mile (seconds) (Estimate) 	13.7 	12.9 	13.8 	12.9	12.9

Top Speed (mph/kph) 	155/250 	155/250 	155/250	155/250	174/280

Max. Power (SAE bhp) @ rpm 	385@6500	510@6000-6500	385@6500	510@6000-6500	510@6000-6500

Max. Power (EEC PS) @ rpm 	385@6500	510@6000-6500	385@6500	510@6000-6500	510@6000-6500

Max. Power (EEC kW) @ rpm	283@6500	375@6000-6500	283@6500	375@6000-6500	375@6000-6500

Power to Weight Ratio – SAE BHP/ton 	236 	296 	231 	288	296

Power to Weight Ratio – EEC PS/tonne	236	296	231	288	296

XK Coupe 	XKR Coupe	XK Convertible 	XKR Convertible	XKR Coupe

5.0L V8 NA	5.0L V8 SC	5.0L V8 NA	5.0L V8 SC	with Speed Pack

5.0L V8 SC

Torque (SAE lb-ft) @ rpm 	380@3500	461@2500-5500	380@3500	461@2500-5500	461@2500-5500

Torque (EEC Nm) @ rpm 	515@3500	625@2500-5500	515@3500 	625@2500-5500	625@2500-5500

Torque to Weight Ratio – SAE lb-ft/ton	233	267	228	260	267

Torque to Weight Ratio – EEC Nm/tonne 	233 	267	228 	260	267

Aerodynamics (Cd) 	0.33 	0.33 	0.35 	0.35	0.33

ECONOMY

Urban (mpg) 	16.5 	14.9	16.5 	14.9	14.9

Urban (l/100km) 	17.1 	18.9 	17.1 	18.9	18.9

Extra Urban (mpg) 	35.3 	33.0 	35.3 	33.0	33.0

Extra Urban (l/100km) 	8.0 	8.6	8.0 	8.6	8.6

Combined Fuel Economy (mpg) 	25.2 	23.0	25.2 	23.0	23.0

Combined Fuel Economy (l/100km) 	11.2 	12.3 	11.2 	12.3	12.3

Fuel Economy - City EPA 	TBC 	15.0	TBC	15.0	15.0

Fuel Economy - Highway EPA 	TBC	22.0	TBC	22.0	22.0

US C-H Combined (mpg - US) 	TBC	17.0	TBC	17.0	17.0

Fuel Tank Capacity (litres) 	71.0 	71.0	71.0	71.0	71.0

Fuel Tank Capacity (USA gallons) 	16.1 	16.1	16.1	16.1	16.1

NEDC Combined CO2 (g/km) 	264	292 	264 	292	292

Emissions 	ULEVII/TIERII BIN5/EUV	ULEVII/TIERII BIN5/EUV	ULEVII/TIERII BIN5/EUV	ULEVII/TIERII BIN5/EUV	ULEVII/TIERII BIN5/EUV

DIMENSIONS

Boot (litres) - with Jaguar Tyre Repair System 	n/a 	n/a	n/a 	n/a	n/a

Boot (litres) - with Space Saver 	330	330 	313	313	330

Wheelbase (inches) 	108.3 	108.3	108.3	108.3	108.3

Wheelbase (mm) 	2752 	2752 	2752 	2752	2752

Front Track (inches) 	61.4 	61.4 	61.4 	61.4	61.4

Front Track (mm) 	1560 	1560 	1560 	1560	1560

Rear Track (inches) 	62.8-63.3 	62.8-63.3	62.8-63.3	62.8-63.3	62.8-63.3

Rear Track (mm) 	1596-1608	1596-1608 	1596-1608	1596-1608	1596-1608

Overall Length (inches) 	188.7 with plinth 	188.7 with plinth	188.7 with plinth	188.7 with plinth	188.7 with plinth

Overall Length (mm) 	4794 with plinth 	4794 with plinth 	4794 with plinth 	4794 with plinth	4794 with plinth

XK Coupe	XKR Coupe	XK Convertible	XKR Convertible	XKR Coupe

5.0L V8 NA	5.0L V8 SC	5.0L V8 NA	5.0L V8 SC	with Speed Pack

5.0L V8 SC

Overall Width (inches) excl. mirrors 	74.5 	74.5	74.5	74.5	74.5

Overall Width (mm) excl. mirrors 	1892	1892	1892	1892	1892

Overall Width (inches) incl. mirrors 	79.8 	79.8	79.8	79.8	79.8

Overall Width (mm) incl. mirrors 	2028	2028	2028	2028	2028

Overall Height (inches) 	52.0 	52.0 	52.3 	52.3	52.0

Overall Height (mm) 	1322 	1322 	1329 	1329	1322

Driver/Passenger Head Room (inches) 	37.4 	37.4 	37.8 	37.8	37.4

Driver/Passenger Head Room (mm) 	950 	950	959 	959	950

Driver/Passenger Leg Room (inches) 	43.0 	43.0 	43.0 	43.0	43.0

Driver/Passenger Leg Room (mm) 	1091 	1091 	1091 	1091	1091

Rear Head Room (inches) 	30.2 	30.2 	33.1 	33.1	30.2

Rear Head Room (mm) 	767 	767 	840 	840	767

Rear Leg Room (inches) 	27.6 	27.6	27.6	27.6	27.6

Rear Leg Room (mm) 	700	700 	700 	700	700

DRIVING DYNAMICS

Tightest Turning Radius Kerb to Kerb (feet) 	35.8 	35.8	35.8	35.8	35.8

Tightest Turning Radius Kerb to Kerb (m) 	10.9 	10.9 	10.9 	10.9	10.9

WEIGHT

EU: Kerb Weight (lbs) 	3651 	3865	3739	3968	3885

EU: Kerb Weight (kg) 	1660 	1753	1696 	1800	1762

Federal: Lightest Weight (lbs) - actual kerb weight 	3770 	3968 	3924 	4079	3988

Federal: Lightest Weight (kg) - actual kerb weight 	1710 	1800 	1780 	1850	1809

Gross Vehicle Weight (lb) 	4575 	4729 	4674 	4817	4749

Gross Vehicle Weight (kg) 	2075	2145 	2120 	2185	2154

Trailer Max Load (kg) 	n/a 	n/a 	n/a 	n/a	n/a